MAKECHAR.DOC: CUSTOM SCREEN CHARACTERS FOR THE Z88
--------------------------------------------------

The Z88 has the capability to implement up to 64 custom characters in 
Basic -- which can then be used for applications where graphics are of 
benefit.

These characters are defined by a VDU statement of the form:

    VDU 1,138,ASC"=",ASC"char",n0,n1.n2,n3,n4,n5,n6,n7

The '138' tells the interpreter that there are 10 more characters in 
the line (138 = 128+10), and 'char' is the ascii character (@ to DEL, 
that is CHR$(64) to CHR$(127)) to which this newly-defined character is 
assigned.

To print this special character to the screen, the syntax is:

      VDU 1,ASC"2",ASC"?",ASC"char"

Following is a "complete" program to generate a happy face and then 
print it:

     #B
     .J
     NEW
     10 VDU 1,138,ASC"=",ASC"@",27,27,0,4,4,17,14,0
     20 VDU 1,ASC"2",ASC"?",ASC"@"

In this example, 'char' has been defined as '@' or CHR$(64).

The characters are defined in a 6 column by 8 row matrix.  The rows are 
defined by the numbers n1 to n7 in downward sequence (n7 is the bottom 
row) and the columns are defined by the six lower bits of the binary 
form of these numbers (bit 0 is the right-most column).  It appears 
that the setting of the two highest bits the the n's is not important.

For example, in the short program above, the bit map is as follows

      00011011 <-- n0
      00011011
      00000000
      00000100
      00000100
      00010001
      00001110
      00000000 <-- n7 (good to have this blank for consistency with Z88
        |              internal characters)
        |
        |<-- A blank column here will avoid butting up to adjacent 
             character.

So, to make your own characters, simply make the pattern you want in 
terms of 1's and 0's and convert the resulting binary numbers to 
decimal.  Then build a set of VDU defining statements like the one at 
the beginning of this file, and you are in business!  Over a period of 
time, a library of such characters can be assembled for general use.

To aid in the process, I have uploaded a program called BASES.CLI.  It 
will do general base conversion; for this application, define the input 
base as 2 and the output base as 10.

There is one major restriction: To use a full set of 64 user-defined 
characters, you must have a minimum of 128K RAM in SLOT 1.  This gives 
you an expanded machine.  Otherwise, you are limited to 16 such 
characters, still a usable quantity.

------------
Phil Wheeler
Torrance, CA
23 Dec 1988