NOTES ON ROMDMP.CLI
-------------------

ROMDMP.CLI is a Z88 Basic program packaged as a CLI file.  After loading it
into your Z88, EXecute it from the filer menu, then save it as ROMDMP, with
or without a BAS extension.

This program appeared in the Sept-Oct 1988 issue of Z88 EPROM, a British
Z88 newletter.  However it had some omissions and errors, as noted in the
REM's of the program.  These have been corrected in the version here.

The address space accessible by the Z80 in the Z88 is on the order of 4 MB.
This is accomplished by paging the memory in 16KB "chunks", with four such
chunks in play at any one time.  This program lets you select any available
page for display as the fourth active chunk.

All I/O is in Hex.  Inputs are the page number 00h to FFh (input just as 6
or F or AF or whatever) and the range of memory to be dumped (always
starting at C000h or above and ending at FFFFh or below, a 16KB range).

Outputs are in a "standard" dump format, with both hex and ASCII formats
(the original program gave truncated decimal instead of hex, and had a
syntax error as printed).  Following is a segment of the dump of Page 6,
which contains the Basic interpreter, among other things:

DAD0:  B0 CD 47 E1 C3 19 DA 80  41 4E 44 94 41 42 53 95   0MGaC.Z.AND.ABS.
DAE0:  41 43 53 96 41 44 56 41  4C 97 41 53 43 98 41 53   ACS.ADVAL.ASC.AS
DAF0:  4E 99 41 54 4E C6 41 55  54 4F 9A 42 47 45 54 00   N.ATNFAUTO.BGET.
DB00:  D5 42 50 55 54 00 FB 43  4F 4C 4F 55 52 FB 43 4F   UBPUT.{COLOUR{CO
DB10:  4C 4F 52 D6 43 41 4C 4C  D7 43 48 41 49 4E BD 43   LORVCALLWCHAIN=C
DB20:  48 52 24 D8 43 4C 45 41  52 00 D9 43 4C 4F 53 45   HR$XCLEAR.YCLOSE
DB30:  00 DA 43 4C 47 00 DB 43  4C 53 00 9B 43 4F 53 9C   .ZCLG.[CLS..COS.
DB40:  43 4F 55 4E 54 00 DC 44  41 54 41 9D 44 45 47 DD   COUNT.\DATA.DEG]
DB50:  44 45 46 C7 44 45 4C 45  54 45 81 44 49 56 DE 44   DEFGDELETE.DIV^D
DB60:  49 4D DF 44 52 41 57 E1  45 4E 44 50 52 4F 43 00   IM_DRAWaENDPROC.
DB70:  E0 45 4E 44 00 E2 45 4E  56 45 4C 4F 50 45 8B 45   `END.bENVELOPE.E
DB80:  4C 53 45 A0 45 56 41 4C  9E 45 52 4C 00 85 45 52   LSE EVAL.ERL..ER
DB90:  52 4F 52 C5 45 4F 46 00  82 45 4F 52 9F 45 52 52   ROREEOF..EOR.ERR
DBA0:  00 A1 45 58 50 A2 45 58  54 00 E3 46 4F 52 A3 46   .!EXP"EXT.cFOR#F
DBB0:  41 4C 53 45 00 A4 46 4E  E5 47 4F 54 4F BE 47 45   ALSE.$FNeGOTO>GE
DBC0:  54 24 A5 47 45 54 E4 47  4F 53 55 42 E6 47 43 4F   T$%GETdGOSUBfGCO
DBD0:  4C 93 48 49 4D 45 4D 00  E8 49 4E 50 55 54 E7 49   L.HIMEM.hINPUTgI
DBE0:  46 BF 49 4E 4B 45 59 24  A6 49 4E 4B 45 59 A8 49   F?INKEY$&INKEY(I
DBF0:  4E 54 A7 49 4E 53 54 52  28 C9 4C 49 53 54 86 4C   NT'INSTR(ILIST.L
DC00:  49 4E 45 C8 4C 4F 41 44  92 4C 4F 4D 45 4D 00 EA   INEHLOAD.LOMEM.j
DC10:  4C 4F 43 41 4C C0 4C 45  46 54 24 28 A9 4C 45 4E   LOCAL@LEFT$()LEN
DC20:  E9 4C 45 54 AB 4C 4F 47  AA 4C 4E C1 4D 49 44 24   iLET+LOG*LNAMID$
DC30:  28 EB 4D 4F 44 45 83 4D  4F 44 EC 4D 4F 56 45 ED   (kMODE.MODlMOVEm
DC40:  4E 45 58 54 CA 4E 45 57  00 AC 4E 4F 54 CB 4F 4C   NEXTJNEW.,NOTKOL
DC50:  44 00 EE 4F 4E 87 4F 46  46 84 4F 52 8E 4F 50 45   D.nON.OFF.OR.OPE
DC60:  4E 49 4E AE 4F 50 45 4E  4F 55 54 AD 4F 50 45 4E   NIN.OPENOUT-OPEN
DC70:  55 50 FF 4F 53 43 4C 49  F1 50 52 49 4E 54 90 50   UP.OSCLIqPRINT.P
DC80:  41 47 45 00 8F 50 54 52  00 AF 50 49 00 F0 50 4C   AGE..PTR./PI.pPL
DC90:  4F 54 B0 50 4F 49 4E 54  28 F2 50 52 4F 43 B1 50   OT0POINT(rPROC1P
DCA0:  4F 53 00 CE 50 55 54 F8  52 45 54 55 52 4E 00 F5   OS.NPUTxRETURN.u
DCB0:  52 45 50 45 41 54 F6 52  45 50 4F 52 54 00 F3 52   REPEATvREPORT.sR
DCC0:  45 41 44 F4 52 45 4D F9  52 55 4E 00 B2 52 41 44   EADtREMyRUN.2RAD
DCD0:  F7 52 45 53 54 4F 52 45  C2 52 49 47 48 54 24 28   wRESTOREBRIGHT$(
DCE0:  B3 52 4E 44 00 CC 52 45  4E 55 4D 42 45 52 88 53   3RND.LRENUMBER.S
DCF0:  54 45 50 CD 53 41 56 45  B4 53 47 4E B5 53 49 4E   TEPMSAVE4SGN5SIN
DD00:  B6 53 51 52 89 53 50 43  C3 53 54 52 24 C4 53 54   6SQR.SPCCSTR$DST
DD10:  52 49 4E 47 24 28 D4 53  4F 55 4E 44 FA 53 54 4F   RING$(TSOUNDzSTO
DD20:  50 00 B7 54 41 4E 8C 54  48 45 4E B8 54 4F 8A 54   P.7TAN.THEN8TO.T
DD30:  41 42 28 FC 54 52 41 43  45 91 54 49 4D 45 00 B9   AB(|TRACE.TIME.9
DD40:  54 52 55 45 00 FD 55 4E  54 49 4C BA 55 53 52 EF   TRUE.}UNTIL:USRo
DD50:  56 44 55 BB 56 41 4C BC  56 50 4F 53 00 FE 57 49   VDU;VAL<VPOS.~WI
DD60:  44 54 48 D3 48 49 4D 45  4D D2 4C 4F 4D 45 4D D0   DTHSHIMEMRLOMEMP
DD70:  50 41 47 45 CF 50 54 52  D1 54 49 4D 45 01 4D 69   PAGEOPTRQTIME.Mi


NOTE: The versions of ROMDMP downloaded after 1/6/89 will show some
differences in the rightmost (ASCII) field.  The original program 
stripped the high bits before calculating the ASCII characters, so that
oddities occured -- like EF above being interpreted as a lower case 'o'; 
the revised versions will print '.' for all characters above 127 (1Fh),
the more standard approach.

This segment contains the Basic keywords, and may even indicate some
undocumented features.

Of particular interest in the program itself is the area from line 330 to
460, an example of using the BBC Basic built-in assembler -- and line 110
which calls the resulting M/L routine.  This shows the use of this largely
undocumented capability in a real application.


Phil Wheeler
Torrance, CA
12/20/88
Rev: 1/7/89