Fixes put into the Better Board (Big Board II) ROMs

As of 07-0-85:
1   Moved scroll code out of VSYNC interrupt to speed up the execution.
2   Made the bell turn-off an interrupt service (4Hz) function.
	The combination of the above two allows operation at better
	than 9600 baud without any character loss!
3   Disable the VSYNC interrupt during CLRLINE.  This prevents
	the block move from sometimes copying the cursor into the line.
4   Move the setting of MOVECS in SETCSR to before the CTC is
	enabled.  This should prevent some strange cursor placement.
5   Moved the 6845 setup tables to CRTTABLE.EQU.  This will allow easier
	updates of other peoples code, while leaving their edited tables
	to remain.
6   Added equates and hooks to support either CRC, or Checksum, or no
	power-up testing.  When no testing selected, optional ROM
	at 1000H is tested for two jumps at the beginning.
7   Fixed handling of NULLS inside of ESCAPE sequences.